## Slide 1
Data Generation Per Observation
Observation Type | Data Rate (kbps) | Duration (Hours) | Total Data (MB)
Max | Min | Max | Min
Continuous Instruments | 2.13 | 0.95 | 24 | 23.0 | 10.3
XNAV Flyby | 0.38 | 0.19 | 1 | 0.2 | 0.1
Gamma Ray Spectrometer Flyby | 0.50 | 0.25 | 0.17 | 0.038 | 0.019
Pushbroom Imager | 218.18 | 184.62 | 0.17 | 16 | 14
Continuous E-Antenna RF | 80.00 | 1 | 36.0
Smart E-Antenna RF (1min/hr) | 1.33 | 24 | 14.4
Continuous SCM | 40.00 | 1 | 18.0
Smart SCM (1min/hr) | 0.67 | 24 | 7.2
Doppler Seismology Average | 0.50 | 0.17 | 0.5
Framing Image Type | Data Per Image (MB) | Integration Time (s) | km/pix @ 100Mm ~4Ru
Max | Min
Default Resolution Image Data Volume
VIS/NIR Full Spectral | 65.5 | 32.8 | 60 | 2
MIR Full Spectral | 8.2 | 4.1 | 60 | 4
PanVIS | 0.5 | 0.5 | 5 | 1
Lossless Doppler w/ lossy brightness map | 0.5 | 60 | 2
3 VIS/NIR | 0.1 | 0.05 | 60 | 2
Diffraction Limited Drizzle Integration Image Data Volume
VIS Full Spectral | 436.7 | 218.7 | 3600 | 0.3
NIR Full Spectral | 181.9 | 91.1 | 2400 | 0.72
MIR Full Spectral | 10.3 | 5.1 | 1800 | 3.2
PanVIS | 1.7 | 1.7 | 100 | 0.3
3 Color VIS/NIR | 0.3 | 0.1 | 1000 | 0.72
Compressed Data Rate Calculations
Instrument | Compression Factor | Compressed Data Rate (kbps) | Duty Cycle
Min | Max | Max | Min
Pushbroom Color VIS | 11 | 13 | 218.2 | 184.6 | Flyby
Gamma Ray Spectrometer | 4 | 8 | 0.5 | 0.3 | Flyby
Laguimir Probe | 4 | 8 | 0.3 | 0.1 | Continuous
Dust Detection | 4 | 8 | 0.1 | 0.1 | Continuous
10 kHz - 1.7 MHz LFR | 3 | 3 | 40.0 | 40.0 | Smart
1.3 MHz - 19.2 MHz HFR | 3 | 3 | 40.0 | 40.0 | Smart
Search Coil Magnetometer | 3 | 3 | 40.0 | 40.0 | Smart
Fluxgate Magnetometer | 4 | 20 | 0.4 | 0.1 | Continuous
SWEAP SPAN-A/B | 8 | 16 | 1.0 | 0.5 | Continuous
EPI-Lo | 8 | 16 | 0.4 | 0.2 | Continuous
XNAV X-Ray Telescopes | 4 | 8 | 0.4 | 0.2 | Flyby
Data Handling Computer
COTS Product and Capabilities
The Xiphios Q8JS system on a chip was selected for scientific data processing. It is rated for 30 krad lifetime radiation and designed expressly for high power edge computation on spacecraft such as real time hyperspectral image compression and artificial intelligence.
Radiation Hardening In Software
The Current Space Born Computer Experiment Series on the ISS has and is demonstrating active radiation hardening using fault detection software and supporting science investigations. The techniques developed allow more powerful and efficient but less radiation hardened computers to be used for onboard scientific data handling.
Data Compression Algorithms
Hyperspectral Image Compression
Hyperspectral Images are first transformed into a spectral principal component domain by performing PCA on all the pixels in a phase space with a dimension for the normalized intensity of each wavelength band. Anomalous pixels, defined as insufficiently sparse in the PCA domain, are saved externally and replaced in the image with imputed values. The image is then compressed to 1 bit per pixel per band in the PCA domain using JPEG XR.
B. Penna, et al, “Hyperspectral image compression employing a model of anomalous pixels” IEEE Geosci. Remote Sens. Lett. 4(4), 664 (2007)
Quantized Chebyshev Transform
The Chebyshev Transform is related to the Fourier transform as a universal basis. Unlike high order Fourier approximations which concentrate error at extrema, Chebyshev approximations spread error evenly. This minimizes the maximum absolute error and preserves extrema more effectively than a Fourier approximation for a given level of quantization.
S.Edward Hawkins III, et al, “A new compression algorithm for spectral and time-series data,” Acta Astronautica
Smart Quantization and Bitshuffle
Fields suite spectral data is compressed by first quantizing the spectral intensities while minimizing the loss of useable signal. The quantized data consists of strings of very similar numbers. Bitshuffle interleaves the data at the bit level to group all the 1s places, 2s places, etc such that a simple lossless compression algorithm, such as LFZ, can easily take advantage of the redundancies present in radiometric data.
Kiyoshi Masui, “A compression scheme for radio data in high performance computing”

## Slide 2
Initial Science Orbit Nominal Measurement Plan
Measurement | Base Duration | Quantity | Data (MB)
Uranus Flyby (<5 Ru)
XNAV Flyby Max | 1 hr | 2 | 0.3
Gamma Ray Spectrometer Flyby Max | 10 mins | 9 | 0.3
Pushbroom Imager Max | 10 mins | 9 | 147.3
Continuous E-Antenna RF | 1 hr | 2 | 72.0
Continuous SCM | 1 hr | 2 | 36.0
Doppler Images | 1 min | 10 | 5.0
Subtotal |  |  | 260.9
Close Orbit (±5 Days of Periapsis)
Continuous Instruments Max | 1 day | 10 | 229.5
Smart E-Antenna RF (1min/hr) | 1 day | 20 | 288.0
Smart SCM (1min/hr) | 1 day | 20 | 144.0
Full Spectral Images Max | 1 min | 4 | 296.8
MIR Full Spectral Images Max | 1 min | 10 | 82.0
Doppler Images | 1 min | 20 | 10.0
3 Color VIS/NIR Max | 20s | 20 | 2.0
Subtotal |  |  | 1052.3
Distant Orbit (20 days)
Continuous Instruments Min | 1 day | 20 | 205.2
Smart E-Antenna RF (1min/hr) | 1 day | 20 | 288.0
Smart SCM (1min/hr) | 1 day | 20 | 144.0
Compressed Sensing Doppler Seismology | 10 min | 120 | 60.0
3 Color VIS/NIR Max | 10 min | 120 | 12.0
DRIZZLE Panchromatic Max | 2 min | 20 | 33.3
DRIZZLE 3 Color Max | 20 min | 10 | 2.8
Subtotal |  |  | 745.3
Total |  |  | 2058.6
Moon Flyby Nominal Measurement Plan
Measurement | Base Duration | Quantity | Data (MB)
XNAV Flyby Max | 1 hr | 1 | 0.2
Gamma Ray Spectrometer Flyby Max | 10 mins | 2 | 0.1
Pushbroom Imager Max | 10 mins | 2 | 32.7
Continuous E-Antenna RF | 1 hr | 1 | 36.0
Continuous SCM | 1 hr | 1 | 18.0
Full Spectral Images Max | 1 min | 4 | 296.8
MIR Full Spectral Images Max | 1 min | 10 | 82.0
DRIZZLE Panchromatic Max | 2 mins | 20 | 33.3
DRIZZLE 3 Color VIS/NIR Max | 20 mins | 20 | 5.6
Totals: |  |  | 504.7
Moon Tour Orbit Monthly Nominal Measurement Plan
Measurement | Base Duration | Quantity | Data (MB)
Continuous Instruments Min | 1 day | 30 | 307.8
Smart E-Antenna RF (1min/hr) | 1 day | 30 | 432.0
Smart E-Antenna RF (1min/hr) | 1 day | 30 | 216.0
Continuous E-Antenna RF | 1 hr | 8 | 288.0
Full Spectral Images Max | 1 min | 6 | 445.2
DRIZZLE MIR Spectral Image Max | 30 mins | 6 | 30.8
DRIZZLE Panchromatic Max | 2 mins | 20 | 33.3
DRIZZLE 3 Color VIS/NIR Max | 20 mins | 20 | 5.6
Totals: |  |  | 1758.6
Data Collection Algorithms
Smart Data Collection for RF and SCM
The smart data collection system is motivated by two goals. The first is to capture unpredictable transient phenomena such as lighting and magnetoplasma interactions. The second is to determine the periodicity of changes such as radio sources rotating into view or repeating magnetic field structures to make the most efficient use of more detailed investigations. The smart data collection algorithm collects data continuously to a rolling buffer, saving “snips” from the buffer that encapsulate data segments with high variance to capture short duration events and sudden changes in the baseline. The system will additionally save a short “snip” if the baseline drifts significantly from the previous “snip”
Compressed Sensing for Doppler Seismology
Compressed Sensing is a set of techniques for reconstructing data that is sparse in a know basis set from a limited number of observations with precisely known random placements. We can assume that the global oscillations of Uranus are sparse in the set of spherical harmonics, and therefore dramatically reduce the data required to measure them compared to nyquist sampling.
DRIZZLE Superresolution Imaging
DRIZZLE is an algorithm for combining many images with relative pointing known to sub pixel precision into a single higher resolution image, up to the diffraction limit of the optics. It was originally developed for the hubble deep field. It allows the sensors’ native resolution to be optimized for imaging Uranus’ atmosphere while still being capable of diffraction limited resolution over long integration times for capturing the slower moving moons and rings.
Relevant Measurement Details
Imaging Science System
VIS Spec: 0.37 - 0.95 μm NIR Spec: 0.95 - 2.3 μm MIR Spec: 2.3 - 10 μm PanVIS: 0.37 - 0.95 μm
Gamma Ray Spectrometer
The Gamma Ray Spectrometer measures gamma ray emissions from light nuclei impacted by cosmic ray fragments. It has a substantially different depth response compared to the ISS spectrometers. It can detect composition 10+ cm below a rocky surface, and consequently deep into an atmosphere. GRS composition measurements can be cross referenced with ISS spectrometer measurements to infer compositional variation with depth in Uranus’ atmosphere and the upper layer of lunar surfaces.
XNAV X-Ray Pulsar Timing
XNAV measures absolute velocity independent of the DSN using pulsars distributed throughout the galactic plane, granting much more pointing flexibility for gravity measurements and allowing them to be conducted in parallel with other pointing dependent measurements.
XNAV also provides an absolute position and velocity reference for spacecraft orbit and moon ephemeris determination. The increased orbit propagation precision presents opportunities to capture stellar occultations of Uranus’ moons that would otherwise too unpredictable.