## Slide 1
Duty Cycles
Continuous: Active except during downlink and main engine burns
Flyby: Active during close approaches
Variable: Active Intermittently as needed for science objectives
Smart: Active Continuously During Close Approaches and as needed for science objectives. Otherwise record data to a buffer and only save snips around high variance events or if the reading is sufficiently different from the most recent snip
Instrument | Mass | Peak Power | Duty Cycle | Raw Data Rate (kbps) | Compression Factor | Compression Algorithm
CBE (kg) | % Cont. | MEV (kg) | CBE (W) | % Cont. | MEV (W)
Orbiter
Imaging Science System | 30.00 | 30 | 39.00 | - | - | - | - | - | - | -
 | VIS/NIR/MIR Spectrometer | - | - | - | 20.00 | 30 | 26.00 | Variable | 106666.00 | 11-23 | Spectral KLT/PCA -> JPEG XR
 | Panchromatic VIS | - | - | - | 8.00 | 30 | 10.40 | Variable | 67108.00 | 11-23 | JPEG XR
 | Pushbroom Color VIS | - | - | - | 8.00 | 30 | 10.40 | Flyby | 2400.00 | 11-23
Gamma Ray Spectrometer | 9.20 | 10 | 10.12 | 16.50 | 10 | 18.15 | Flyby | 2.00 | 4-8 | Quantized Chebyshev Transform
FIELDS Electric Antennas | 5.37 | 10 | 5.91 | - | - | - | - | - | - | -
 | Laguimir Probe | - | - | - | 0.50 | 10 | 0.55 | Continuous | 1.00 | 4-8 | Quantized Chebyshev Transform
 | Dust Detection | - | - | - | 0.50 | 10 | 0.55 | Continuous | 0.50 | 4-8
 | 10 kHz - 1.7 MHz LFR | - | - | - | 1.50 | 10 | 1.65 | Smart | 120.00 | 3 | Smart Quantization -> Bitshuffle -> LFZ
 | 1.3 MHz - 19.2 MHz HFR | - | - | - | 1.50 | 10 | 1.65 | Smart | 120.00 | 3
Search Coil Magnetometer | 0.80 | 10 | 0.88 | 0.60 | 10 | 0.66 | Smart | 120.00 | 3
Fluxgate Magnetometer | 1.43 | 10 | 1.57 | 2.00 | 10 | 2.20 | Continuous | 1.50 | 4-20 | Quantized Chebyshev Transform
2.5m Fields Boom | 0.47 | 20 | 0.56 | - | - | - | - | - | - | -
SWEAP SPAN-A/B | 2.50 | 10 | 2.75 | 2.00 | 10 | 2.20 | Continuous | 8.00 | 8-16 | Spectral KLT/PCA -> Time Series Quantized Chebyshev Transform
EPI-lo | 3.50 | 10 | 3.85 | 2.50 | 10 | 2.75 | Continuous | 3.00 | 8-16
Radio Science Experiment | - | - | - | 30.00 | 10 | 33.00 | Variable | - | - | -
XNAV X-Ray Telescopes | 17.00 | 20 | 20.40 | 16.67 | 20 | 20.00 | Flyby | 1.50 | 4-8 | Quantized Chebyshev Transform
Data Processing Computer | 0.10 | 3 | 0.10 | 25.00 | 3 | 25.75 | Variable | - | - | -
Totals | 70.37 | 13 | 85.15 | 135.27 | 14 | 155.91 |  |  |  | 
 | Peak Flyby Power |  |  |  |  |  | 60.76 |  |  |  | 
Instrument | Mass | Power | Total Data (MB/hr)
CBE (kg) | % Cont. | MEV (kg) | CBE (W) | % Cont. | MEV (W)
Probe
Mass Spectrometer | 16.2 | 10 | 17.82 | 19 | 10 | 20.9 | 9
Atmosphere Structure Instrument | 2.5 | 10 | 2.75 | 3.5 | 10 | 3.85 | 1
Ortho-Para H2 Sensor | 1 | 30 | 1.3 | 3.5 | 30 | 4.55 | 1
Radio Science Experiment | - | - | - | - | - | - | 5
Totals | 19.7 | 17 | 21.87 | 26 | 17 | 29.3 | 16
Instrument Heritage By Mission
MESSENGER | Gamma Ray Spectrometer
Flux Gate Magnetometer
TRACERS | Search Coil Magnetometer
Parker Solar Probe | FIELDS Electric Antennas
SWEAP SPAN-A/B
EPI-lo
NICER SEXTANT, Cube-X, & XPNAV-1 | XNAV
Rosetta | Probe Mass Spectrometer
Huygens | Atmosphere Structure Instrument
Perseverance | Ortho-Para H2 Anemometer
New Technology | Imaging Science System